The calibration issue

Programs required

Tests on ATMEGA 168

Prepare green project pcb with no display and DIP socket.
Put Github_PCB-111000_V2/Mini-OS_V22/Hex_files/CA_files on the fixed device

Plug an Atmega 168 into the DIP and run

1.	Run Github_dev/9_cal_auto_plus_manual/Cal_Atmega_V1
Tests T2 interrupt (remember Baud rate switch)

2.	Run	Github_PCB-111000_V2/.../Proj_9_System_projects/Proj_9A_Plot_ATMEGA168_cal
Tests TWI interrupt

3.	Run	ATMEGA_project_work_BKP_30_July_19/I2C_apps_project_V8/5_Clock_calibration/	Plot_cal_168_V3_5_5ransfer Tests T2 interrupt.

4.	Place the device on the UNO programmer jig and run	Github_dev/9_cal_auto_plus_manual/	Cal_Atmega_V1

Repeat test 1 with 100nF cap across pin 7 and 8 of the device being calibrated
For consistent results it is important to place a 100nF cap across pin 7 and 8 of the device being calibrated. This is particularly important for the programming jigs including PCB 111000.
It is not necessary for PCB111000_1 the plug in pcb for the UNO.

Tests on ATMEGA 328
Github/PCB-111000_1/2_AVR_projects/Proj9D_ATMEGA_plot_cal
This runs on the UNO pcb and plots the cal for the pcb_a device.
T2 interrupt

J	Green project pcb + 100nF
K	UNO Prog_jig + 100nF

Compares use of TWI interrupt with T2 interrupt with original cal computation

Red line shows corruption caused by the absence of decoupling
Corruption on green project pcb is much less but is still clearly visible.

Tolerance to OSCCAL error

Opt value of 78 gives error of -136
Select value of 81 giving an error of 998	OK
Select value of 82 giving an error of 1440	OK
Select value 83 giving an error of 1881	OK
Select value 84 giving an error of 2193	FAILS

Select value 75 giving an error of -1310	OK
Select value 74 giving an error of -1726	OK
Select value 73 giving an error of -2112	OK
Select value 72 giving an error of -2536	OK
70	-3085	FAILS

An acceptable error of +/-1750 (2.8%) has been imposed. Typically this gives up to 8 acceptable calibration values.