Introducing the UNO programmer

An Atmega 328 device pre-loaded with the Arduino bootloader and the UNO hardware make a very effective combination for developing and running C applications. Other programmers have been developed that are more general purpose. For example the USBasp programmer can be used to program the flash and config bytes of a range of AVR devices. The purpose of the development described here is to apply and even extent this flexibility to the UNO.

An Arduino application “UNO_programmer” is introduced that is hosted on the UNO and enables it to be used to program Atmega devices as follows:

Flash with a hex file loaded at address zero.
Flash with a text file loaded from the maximum address.
The configuration bytes.
The EEPROM with text and numbers.

Two Arduino applications are provided for a target device.

The first “Cal_auto_plus_manual” is used calibrates the target device.
The second “text_reader” contain the subroutines needed to read text from the flash.
A sample text file is also provided.

UNO programmer test jig.

A photograph of the test jig is shown below.
The target device is loaded into some plug-in prototyping breadboard.

The following connections between the UNO and target device are made:

UNO		Atmega 328 target Pin number
5V		5V	7 & 20
0V		0V	8 and 22
Rx		USART TXD	3
Tx		USART RXD	2
Digital 11	MOSI	MOSI	17
Digital 12	MISO	MISO	18
Digital 13	SCK	SCK	19

In addition the following extra components are used

A watch crystal between pins 9 and 10 (TOSC1 and TOSC2) of the target device
A 100nF capacitor between pins 7 and 8 of the target device
A led and 1K resistor between digital output 8 (PB0) of the UNO and 0V.

A user interface for the UNO programmer

A PC application normally used for sending hex files to the target processor hardware has not been written. Instead a terminal program is used and the entire hex file is sent to the bootloader. Arduino comes with a basic terminal program and there are several others on the web.
 My favourite can be downloaded from  https://sites.google.com/site/terminalbpp/. But take care to download the version 20130820, other versions may have an issue with the "scroll" button.
Settings for the terminal program are: Baud rate: 38400, 8 data bits, no parity, 1 stop bit and no handshaking.

Running the “UNO_programmer”: Atmega 328 target devices only

Connect the UNO to the PC and open the Arduino application “UNO_programmer”. It should upload OK. Check the comm port number if there are problems.

Open the terminal program.
User prompt “s s s s …..” should be generated.
Left click the mouse in the grey area at the bottom of its window and press ‘s’.
The programmer should respond with the message “Target_not_detected”.

Complete the UNO_programmer test jig and reconnect it to the PC.
This time the response should be “Press -p- to program flash, -e- for EEPROM or -x- to escape.”

Press ‘p’ to program a hex file only.
Click the “Send File” box and send a hex file when requested.
Press ‘0’ at the “Integer(0-FF)?” prompt.
The file size and config bytes should be printed out.

If ‘n’ is pressed at the “Text_file? y or n” prompt the program will run immediately.

To re-initialise the UNO programmer press the UNO reset switch.

If ‘y’ is pressed at the “Text_file? y or n” prompt a text file will be requested and immediately echoed back to the terminal program.

Running the “Cal_auto_plus_manual” applications

Target device calibration	The application “Cal_auto_plus_manual” stores calibration bytes in the top two addresses of the target device eeprom. User applications can do without with the crystal. Instead they will read these bytes and use them to replace the default value of the OSCCAL register.
There is of course no need to restrict the target device to using its internal RC oscillator. However it is the default selection and is in many cases very convenient to do so.

Running the cal application	This is supplied as an Arduino project however uploading it to the target device requires the “UNO programmer” rather than the Arduino bootloader. Its hex file is supplied but if changes are introduced a new hex file can be obtained by clicking on “Sketch/Export compiled Binary” and selecting “UNO_programmer.ino.standard”

To run the application
Connect the test jig to the PC and open the terminal program.
Download the hex file as described above.
There is no text file.
Auto cal will start running automatically.
Press ‘0’ when requested assuming an Atmega 328 or 328P device.
Press ‘x’ to select the new calibration value or any other key to check it.

Reading text from the Flash

Upload the “text reader application” follows by the text file.

jkjkjk

Programming target devices other than the Atmega 328