Test results

CA device:
Reload UNO bootloader
Load “Project_programmer_UNO”
Program pcb-a eeepro
Program pcb_a flash with mini-OS
CA Auto cal result: 160	error 118
CC Auto cal result: 186	error 156
Load Uno Prog_1A1.

Double click pcb_a reset
Press “p, r” to download UNO bootloader

Double click pcb_a reset
Press “p, p” and program UNO with “2_UNO_bootloader_for_hex&text_V6”

At h/t/r/D prompt press “r”
Get default program
Hold sw1 down and pulse sw2 to get hello world strings
Hold sw3 to control brightness.
Power cycle and restore default program

Double click pcb_a reset to get h/t/r/D prompt
Press “t” and download commentary then hex.
Press “r”: Read commentary
Press “X” to start program

Power cycle: note immediate start

Note: Single click gives h/t/r/D prompt: this is wrong: It should restart the program.

Program changes

For the PCB_A device initialise all IO to WPU
i.e.
#define initialise_IO;\
MCUCR &= (~(1 << PUD));\
DDRB = 0;\
DDRC = 0;\
DDRD = 0;\
PORTB = 0xFF;\
PORTC = 0xFF;\
PORTD = 0xFF;\

in
I2C_V18_Header_file_CA.c
I2C_V18_Header_file_CC.c
and
Bootloader_header.h

Define the following signalling macros for use in
I2C_V18_CA and I2C_V18_CC
PCB_A_bootloader_V5_CA and
PCB_A_bootloader_V5_CC

Place in
I2C_V18_Header_file_CA
I2C_V18_Header_file_CC
Bootloader_header

#define Reset_signal_high_CA \	//Default state
DDRB &= (~(1 << DDB1));\
PORTB |= (1 << PB1);

#define Reset_signal_low_CA \	//starts at WPU
PORTB &= (~(1 << PB1));\	//Tri-state
DDRB |= (1 << DDB1);\	//Output low

/*****************************************************************************/
#define Reset_signal_high_CC \	//Default state
DDRB &= (~(1 << DDB2));\
PORTB |= (1 << PB2);

#define Reset_signal_low_CC \	//starts at WPU
PORTB &= (~(1 << PB2));\	//Tri-state
DDRB |= (1 << DDB2);\	//Output low

/***************************************************************************/

#define Reset_UNO_Low \	//starts at WPU
PORTC &=(~(1 << PC3));	//Tri-state
DDRC |= (1 << DDC3);	//Output low

#define Reset_UNO_High \	//starts at Output low
DDRC &= (~(1 << DDC3));\	//Tri-state
PORTC |=(1 << PC3);	//WPU

/***************************************************************************/
In I2C_V18_CA and I2C_V18_CC
Place lines
Initialise_dislay_brightness;
set_digit_drivers;
clear_digits;
clear_display;
initialise_Arithmetic_variables;

after OSCCAL_WV = OSCCAL; (i.e. after UNO has been reset)

/***************************************************************************/
Auto cal post being programmed

Using Project_programmer_Uno to write to 0x3F1 is no-longer required
Auto cal takes place post being programmed or on demand but not after POR.

Set Reset_signal before doing UNO reset

UNO bootloader jumps

Message from mini-OS	0x5C60
Random Gen	0x5E20
Hex_verification	0x61E0
4_Text_Verification_part_4	0x6C30
Bootoader	0x7000

Message from mini-OS	NIJ
Random Gen	asm("jmp 0x5C60");
Hex_verification	NIJ
Text_Verification	NIJ

Bootloader	jmp 0x5E20	Random Gen
jmp 0x0000	User app
jmp 0x5E20	Random Gen
jmp 0x61E0	Hex Verification
jmp 0x6C30	Text verification

Restore Github mode pre auto_cal

Fault in commentary mode
Reprogram from scratch starting with UNO bootloader
Press "r" and run default programs
Press "h" then "r"
Program tries to print non existent commentary and makes a mess.
Think:
UNO bootloader resets UNO EEPROM
If commentary string pointer = 0xFF following programming by bootoader
set it to zero in the
User_app_commentary_mode macro in Project Basic_HW_setup.h file

Operation of commentary mode

Text is save at address 0x5C80
Press "T"
Call "text_programmer()" and exit it
with "eeprom_write_byte((uint8_t*)0x3F4,0x40)"
This resets the string pointer
jmp 0x6C30	"Text_Verification.c"l
Print all strings out and the do WDReset
Give h/t/r/D.... user promprt

Press "t"

call "text_programmer()"
"eeprom_write_byte((uint8_t*)0x3F4,0x40)"
call "hex_programmer()"
jmp 0x61E0	"Hex_verification"
Exit with WDReset
Give h/t/r/D.... user promprt

Press "r"

Run "setup_UNO_extra;"
Run "User_app_commentary_mode;"
eeprom_read_byte((uint8_t*)0x3F4) = 0x40
String_to_PC("Project commentary: Press 'X' to escape or AOK\r\n");
eeprom_write_byte((uint8_t*)0x3F4,0x41);	String counter
Set bit 7 of 0c3F4
jmp 0x6C30	"Text_Verification.c"
Print string
inc 0x3F4
SW reset
Run "setup_UNO_extra;" again and print next string and "waitforkeypress()"
Continue prnting stings untill user presses "X".
eeprom_write_byte((uint8_t*)0x3F4,0); Resets String counter.SW reset

Run "setup_UNO_extra;"
Commentary modde is now skipped

Run the user app.

Get h/t/r/D....
Press "h"
call "hex_programmer()"
jmp 0x61E0	"Hex_verification"
Exit with WDReset
Give h/t/r/D.... user promprt

Press "r"	Tries to print out no existant commentary
Solved with
if(eeprom_read_byte((uint8_t*)0x3F4) == 0xFF)\
eeprom_write_byte((uint8_t*)0x3F4,0);\
lines in
User_app_commentary_mode macro in Project Basic_HW_setup.h file

LED dimmer	Works in user app mode, but not Default App as expected!

A version	Click/double click OK but does not print out cal results

Proj_Programmers:	When deleting target EEPROM delete everything except cal bytes:

PCB_A flash verification	phys_address = 0x2E30;//0x2E48;

Double click fails after power cycle failure
Power cycle while running user app
Use app is OK
h/t/r/D fails
MCUSR &= (~(1 << PORF)); write at the top of 1_PCB_A_Mini_OS_I2C_V18 appears to fix it

Modify original cal_at_POR_routine

Before closing it add
Initialise_I2C_master_write;
I2C_master_transmit(OSCCAL);
I2C_master_transmit(cal_error >> 8);
I2C_master_transmit(cal_error);
TWCR = (1 << TWINT) | (1 << TWEN) | (1 << TWSTO);

ALSO add case 'R': Cal_at_Power_on_Reset(); break; to 1_PCB_A_Mini_OS_I2C_V18

1_PCB_A_Mini_OS_I2C_V18 There is a Clash between “set_digit_drivers;” and “initialise_IO;”.

IO config for CC pcb:
initialise_IO:	Everything WPU except PC3 which is tri-state

set_digit_drivers: Digits PB0,2,3,4,5, and PC0, 1, 2 All initialised to output low

PB2 is the signalling line that needs to default to high
Pin	PORTB	DDRB		PORTC	DDRC		PORTD	DDRD
0	1	1	OH	1	1	OH	1	0	WPU
1	0	1	OL	1	1	OH	1	0	WPU
2	1	1	OH	1	1	OH	0	1	OL
3	1	1	OH	Ext reset ????????????			0	1	OL
4	1	1	OH	1	0	WPU	0	1	OL
5	1	1	OH	1	0	WPU	0	1	OL
6	1	0	WPU	Reset			0	1	OL
7	1	0	WPU	n/a	n/a		0	1	OL

WPUs are
B6 and 7	The crystal
C4 and 5	I2C
D0 and 1	The UART
PB2 is the signalling line for a CC pc
Bootloader headers IO definitions
Initialise all IO to WPU

DDR = 0	Port = 1

#define UNO_reset_cntrl_high_CC \	//DDR = 0	Port = 1 WPU	Default state
DDRB &= (~(1 << DDB2));\	//NO CHANGE
PORTB |= (1 << PB2);	//NO CHANGE

#define UNO_reset_cntrl_low_CC \	//DDR = 0	Port = 1 WPU	Default state
PORTB &= (~(1 << PB2));\	//DDR = 0	Port = 0	Tri-state
DDRB |= (1 << DDB2);\	//DDR = 1	Port = 0	//Output low

#define Reset_UNO_low \
PORTC &= (~(1 << PC3));\
DDRC |= (1 << DDC3);

#define Reset_UNO_high \
DDRC &= (~(1 << DDC3));\
PORTC |= (1 << PC3);

Add Reset_UNO_low;
Post double click if user presses “p” put device into reset immediately to prrevent 5_UNO_bootloader_V6 sending spurious char.
This does not appear to interfere with “Atmel_powerup” macro

I2C_V18_CC.c IO definitions

C3 WPU
B2 OH	Reset_UNO_low	Reset_UNO_high	see table above