PCB111000_1

What is it
It is a simplified version of PCB111000 designed to plug onto an Arduino UNO pcb. It contains the display, the OS device (an Atmega 328 loaded with the mini-OS), user switches and the dual led.
Note: The mini-OS consists of the display driver and PCB bootloader.

The UNO supplies the USB bridge, power and sockets and the user device (an Atmega 328 that hosts an Atmega bootloader and the user projects).

Circuit diagram
Note:
A watch crystal is connected between B6 and B7
The diodes are LEDs
The sockets are used to connect PCB111000_1 to the UNO pcb.
PCB111000_1 is also referred to as PCB_A
The combination of PCB_A plugged into the UNO is referred to PCB111000_UNO

Both PCB_A and the UNO are loaded with Atmega 328 devices, however the UNO device is clocked using a 16MHz resonator and the PCB_A device using its internal 8MHz oscillator. They therefore run under different sets of configuration bytes. This is used to distinguish between the UNO and PCB_A when the flash/EEPROM of their devices is being programmed.

Project system applications

UNO Hex/text bootloader.	This resides in the boot partition of the user device and programmes its flash with hex and text files (it replaces the standard UNO bootloader).

Project programmer.	This programs both EEPROM and flash (hex files only). When running on the UNO device it is used to program the pcb_A device (with the mini-OS or a copy of itself). However when running on the pcb_A device it can not be used to program the flash of the UNO device. This is done using the mini-OS. Two almost identical versions of the project programmer exist. “Project_programmer_AVR.c” is compiled using WinAVR and “Project_programmer_UNO.ino” is compiled using the Arduino development environment. Both versions are identical in all other respects.

Mini_OS	The display controller and I2C master reside in the application partition of the pcb_A device. The PCB-bootloader resides in the boot partition of this device. Its main function is to overwrite the original UNO bootloader with the UNO_Hex/text bootloader. After that it should only rarely be required.

Why interfere with the Arduino code

The UNO comes with a very good bootloader. The idea here however is to combine the UNO with PCB 111000_1 to create a new product k/a PCB 111000_UNO that will replace the original PCB 111000 and be very easy to assemble.

The benefit of having access to programmer code is that each use of the programmer is tailored to an individual requirement. Hopefully this should enable PCB 111000_UNO to perform as a single product rather than the combination of two quite different ones.

Two additional features are also offered: Text programming of the flash and optional verification.
At the h/t/r prompt press h or t for programming without verification and H or T for programming with verification.

EEPROM Reservations

	UNO device	PCB_A device
0x3FF	User cal if set	User cal if set
0x3FE	User cal if set	User cal if set
0x3FD	Default cal supplied by Atmel	Default cal supplied by Atmel
0x3FC	Copy of MCUSR	Diagnostic mode
0x3FB	prog_counter_H	Multiplexer period
0x3FA	prog_counter_L	Not used
0x3F9	cmd_counter_H	Reset status_1
0x3F8	cmd_counter_L	prog_counter_H
0x3F7	Reset control	prog_counter_L
0x3F6	PRN EEPROM reservation UNO_bootloader	cmd_counter_H
0x3F5	PRN EEPROM reservation UNO_bootloader	cmd_counter_L
0x3F4	Flash text string pointer	Reset_status_2
0x3F3	8 bit PRN gen user app	8 bit PRN gen EEP subroutines
0x3F2	16 bit PRN gen user app
0x3F1	WDTout detected	Signals Auto cal

Note: reset status is written by the Project Programmer to indicate a device has just been programmed.

ARDUINO UNO connections
Refer to circuit diagram at the beginning of this document.

SK1		SK2		SK3		SK4
1	D0 RXD	1	B0	1	C5 SCL	1
2	D1 TXD	2	B1	2	C4 SDA	2	0V
3	D2	3	B2	3	C3	3	0V
4	D3	4	B3 MOSI	4	C2	4	5V
5	D4	5	B4 MISO	5	C1	5	3V3
6	D5	6	B5 SCK	6	C0	6	C6 RESET
7	D6
8	D7

PCB111000_1/Arduino interconnections

Note:
The Arduino_UNO (to be k/a the UNO) contains the user IC, the one that hosts user projects and Atmega bootloader. PCB111000_1 (to be k/a pcb_A) contains the IC that hosts the mini-OS.

PCB111000_1	UNO
SW1	B2	User switches
SW2	D7
SW3	D2
SW4 C6 RESET	C3	Resets mini-OS/programmer IC
R8	B0	Dual LED driver
R9	B1
R14	C4 SDA	I2C bus
R15	C5 SCL
B3	B3 MOSI	Bi directional programming interface
B4	B4 MISO
B5	B5 SCK
C3	C6 Reset	Resets the user IC
B1	D5	Reset SW control for a CA display
B2	D6	Reset SW control for a CC display

PCB111000_1 Display connections

Segments	Port	Digits	Port
A	B1	1	B5
B	D2	2	C0
C	D3	3	C1
D	D4	4	C2
E	D5	5	B0
F	D6	6	B2
G	D7	7	B3
		8	B4

UNO device fuse settings (as delivered and as used in this project)

Extended	0x5	2.7V BOD	OK
High	0xDE	as delivered	Change to 0xD0
1	Ext reset
1	Debug off
0	Serial programming
1	WDT under program control
1	Eeprom not saved at chip erase	Change to zero
1	Minimum boot partition size	Change to zero
1	Minimum boot partition size	Change to zero
0	Reset vector to boot partition 0x7000

Low	0xFF	16MHz low power resonator, 64mS SUT	OK

PCB_A device fuse settings

Extended	0xFD (i.e. 0x5)
High	0xD0
Low	0xE2	64mS SUT internal 8MHz oscillator.

Display segment currents

For 560R resistors the current per segment is 4.3mA (pd of 2.4V accros 560R)

For 220R resistors the current per segment is 9.1mA (pd of 2V accros 220R)

Consider the display 88888888:
The constant current in each 220R resistor is 9.1mA
The current to be sunk by the appropriate I/O pins is 64mA however the duty cycle is only 1in 8 i.e. 12.5% and the mean current is mA well within the IC max limits.
Display absolute max dc current is 30mA
TEST Procedure
Setting up PCB 111000_UNO

Basic set up	Using Project_programmer_UNO only
Start with a UNO pcb running the Arduino bootloader.

Open the Arduino GUI:	Use it to upload Project_programmer_UNO onto the UNO device.

Open a terminal emulator:	Run Project programmer_UNO. Use it to program the PCB_A device EEPROM with the Hello_world file and flash with PCB_A_Mini_OS_I2C_V17_CC/CA.

Close the emulator:	Upload Proj_1A1_UNO using the Auduino GUI. This clears
Project_programmer_UNO from the UNO device and checks the operation of the display.

Re-open the emulator:	Double click PCB__A reset switch so that the display stops operating.
Press key ‘p’ so that a ‘?’ is displayed on the emulator.
Then press key ‘r’ which starts a download of the Arduino bootloader from the UNO device.
Save the bootloader for later use.
Double click the reset switch again.
This time press ‘p’ followed by ‘p’ and upload “UNO_bootloader_for_hex&text_V5”.

The “h/r/t/D...” user prompt is automatically generated.

Use ‘r’ to run the default programs
Press sw1 and pulse sw2 to read hello world strings
Press sw3 to operate intensity control

Double click the reset switch
Use ‘h’ and ‘t’ to upload programs and their commentaries.
Use ‘r’ to display the commentaries and run the programs
r
Power cycle and check that the user app starts up automatically.

Use ‘D’ to reinstate the default programs

Check that a single click of PCB_A reset switch resets the user app. And a double click gives the “h/r/t/D...” user prompt

Having got the user prompt make keypress ‘p’ followed by ‘q’ and restore the original UNO bootloader to the UNO device. Upload Proj_1A1_UNO and check that it works correctly.

Done for PCB 111000_UNO/CA
Done for PCB 111000_UNO/CC

/********************************************************************************/
Setup using a Project_programmer on both devices

Start with the UNO pcb device running the Arduino bootloader.
Open the Arduino GUI:	Use it to upload Project_programmer_UNO onto the UNO device.

Open a terminal emulator:	Launch Project programmer_UNO. Use it to program the PCB_A device with Project programmer_AVR
Note that Project programmer_AVR running on PCB_A launches automatically and the baud rate should immediately be reduced to 28800.
Program the UNO device EEPROM after which control automatically passes back to Project programmer_UNO and a 56700 baud rate is required.
Pressing ‘s’, ‘x’ reinstates Project programmer_AVR running on PCB_A and requires a 28800 baud rate.
Pressing ‘s’, ‘x’ again reinstates Project programmer_UNO and requires a 57600 baud rate.
As an alternative holding PCB_A in reset when Project programmer_AVR is running forces Project programmer_UNO to run.

Attempt to program the UNO device flash. Note that this is not allowed (because of a config bytes incompatibility)

Launch Project programmer_UNO, select 57600 baud rate press ‘s’ ‘p’. Program PCB_A with PCB_A_Mini_OS_I2C_V17_CC/CA.

Upload Proj_1A1_UNO using the Auduino GUI. This clears Project_programmer_UNO from the UNO device and checks the operation of the display.
Double click PCB_A reset switch and download the original Arduino bootloader code.
Double click PCB_A reset switch and upload “UNO_bootloader_for_hex&text_V5”.

Continue tests as for the basic setup.

Done for PCB 111000_UNO/CA
Done for PCB 111000_UNO/CC

/******************************************************************************/
Upgrading firmware without recourse to the Arduino GUI

Start with PCB_A_Mini_OS_I2C_V17_CA/CC and UNO_bootloader_for_hex&text_V5 running.

Put Project programmer_AVR on both devices
At the h/t/r/D… prompt press “h” and put Project programmer_AVR on the UNO device
At the h/t/r/D… prompt press “rsp” and put it on the pcb_a device.
Reduce the bad rate to 28800 th restore the s...s…...s…… prompt
Press “s” to get 2ATMEGA (UNO)328P detected” message

Press ‘s’ ‘x’ to swap between programs running on UNO and PCB_A
or
When PCB_A is running hold it in reset to force UNO to run
s
Put “hello world” strings on UNO.
Note: we are not able to program the UNO this way

With UNO running restore PCB_A_Mini_OS_I2C_V17_CA/CC to PCB_A.

Double click PCB_A reset switch then press ‘p’ ‘p’ and update the UNO SW.

Press ‘r’ and check that the default programs run OK.

Restore UNO OS and Upload Proj_1A1_UNO to restore normal operation.

Done for PCB 111000_UNO/CA
Done for PCB 111000_UNO/CC

Mistaken case	At the UNO_update? Prompt program something like Proj_1A1.
It may or may not work and there will be no bootloader.
Double click PCB_A reset switch press p p and try the update again.

Calamity case	At UNO_update prompt send Project_programmer so deleting the UNO bootloader.

Run the Project_programmer on the UNO device and use it to put Project programmer_AVR-rescue on pcb_a. Use this to restore UNO_bootloader_for_hex&text_V5 to the UNO device.

Then

Pulse PCB_A reset to get R prompt
Press and hold it again to get h/t/r/D prompt
press h and reload Project programmer_AVR on the UNO device.
Press r then s and release reset switch
Reload PCB_A mini-OS and get h/t/r/D…….user prompt and immediately press D

This will delete the Project_programmer from the UNO device giving the default programs.
T

Second Calamity case	Its not possible to get the h/t/r/D…. prompt.

Happened after running “Proj_9C_ATMEGA328_manual_cal” but not sure why.
Believe eeprom may have got corrupted.

“Proj_9C_ATMEGA328_manual_cal” exits with the following message
Enter new user cal value or
enter zero to delete the user cal or
press the reset switch if OK.
ALWAYS exit with the R...R...R prompt: press reset switch if necessary

Was a struggle to fix but eventually the following procedure did it.

Using a second UNO/pcb_a pair
Put “Project_programmer_AVR” on the UNO
Put “Project_programmer_AVR_rescue” on the pcb_a
At the reset prompt put “Proj_1A_AVR” on the UNO to get rid of “Project_programmer_AVR”

Take the failed UNO/pcb_a pair and remove pcb_a
Replace it with the pcb_a hosting “Project_programmer_AVR_rescue”

At the R….R prompt press R and reprogram the UNO with “2_UNO_bootloader_for_hex&text_V6”
At the s...s….s prompt press s and reprogram pcb_a with 1_PCB_A_Mini_OS_I2C_V18
At the h/t/r/D prompt press t and program Proj_1A commentary and hex.
Press r to get the commentary
Press X to run the program

Publicity

AVR freaks

https://circuitdigest.com/editorial

Arduino projects